## Slide 1: Interpretation of Air Quality Indices and Reporting
Victoria Owusu-Tawiah
Kigali Collaborative Research Centre

## Slide 2
PRESENTATION OUTLINE
Introduction
AQI and Its Relevance
Key Pollutants
AQI calculation, Categories and Color Coding
Health Implications
Importance of AQI Interpretation
Conclusion

## Slide 3
INTRODUCTION
Air quality affects health, environment, and policy decisions.
The Air Quality Index (AQI) is a standardized tool used worldwide.
Notes: The Global Air Quality Forecasting and Information System (GAFIS) project, a new initiative by the WMO Global Atmospheric Watch (GAW) program is aimed at providing globally harmonized air quality forecasts tailored to the needs of end users.
The World Health Organization (WHO) attributes millions of premature deaths annually to exposure to ambient PM2.5

## Slide 4
WHAT IS AQI?
A numerical scale that communicates how clean or polluted the air is.
Ranges typically from 0–500.
Higher value = greater health risk.

## Slide 5
PURPOSE OF AQI
Simplifies scientific air-quality measurements.
Helps the public make decisions about outdoor activities
Guides government health advisories.
Enables consistent reporting across regions.

## Slide 6
KEY POLLUTANTS USED IN AQI
Particulate Matter (PM2.5 & PM10)
Ozone (O₃)
Nitrogen Dioxide (NO₂)
Sulfur Dioxide (SO₂)
Carbon Monoxide (CO)

## Slide 7
HOW AQI IS CALCULATED
Let’s calculate the AQI for PM2.5 when its measured concentration is 40 µg/m³.
From the AQI table, 40 µg/m³ falls in the "Unhealthy for Sensitive Groups" category (35.5 - 55.4 µg/m³), with an AQI range of 101 - 150.
Using the formula:
AQI = [(150 - 101) / (55.4 - 35.5)] * (40 - 35.5) + 101
AQI = [(49) / (19.9)] * (4.5) + 101
AQI ≈ 112
So, the AQI for PM2.5 at 40 µg/m³ is approximately 112, meaning the air quality is "Unhealthy for Sensitive Groups

## Slide 8
COLOR-CODING SYSTEM AND HEALTH IMPLICATIONS
Image Source: Metro Manila Air Quality Index (AQI)
Green Yellow Red Pink Purple Maroon

## Slide 9
TOOLS FOR MONITORING AQI
Real-time dashboards and mobile apps.
Ground-based sensors (EPA, national agencies)
Satellite data (e.g., Sentinel-5P, MODIS)
Low-cost community sensors.

## Slide 10
REPORTING STANDARDS
Daily or hourly reporting depending on region
  Must Include:
      Location
      Timestamp
      Pollutant Concentration
      AQI Category + Health Message

## Slide 11
CHALLENGES IN AQI REPORTING
Low data coverage in some regions
Public misunderstanding of technical terms
Variability in standards across countries
Sensor Calibration and accuracy issues

## Slide 12
IMPORTANCE OF AQI REPORTING
Supports public health protection
Helps city planners and policymakers
Builds environmental awareness
Essential for early-warning systems

## Slide 13
CONCLUSION
AQI is a powerful tool that converts complex air-quality measurements into simple, actionable information
Effective interpretation and reporting help safeguard health and guide community decisions.
Accurate communication = stronger environmental risk management.

## Slide 14
Assessment of PM₂.₅ exposure risk levels Using AQI

## Slide 15
Diurnal Variations of AQI across the six schools

## Slide 16
THANK YOU
Victoria Owusu Tawiah
vikowusu@gmail.com