## Slide 1: AIR QUALITY STANDARDS & REGULATORY FRAMEWORK AND POLICIES IN GHANA
ING. SELINA O. AMOAH
AG. DIRECTOR/ ENVIRONMENTAL QUALITY UNIT

## Slide 2: OUTLINE
Standard and why the need
Air Quality Standards
Standard Development Process
Legal & Regulatory Framework
Air Quality Management Efforts by EPA
Challenges
Way Forward

## Slide 3: STANDARD
Standards are published documents that establish specifications and procedures designed to ensure the reliability of materials, products, methods, and/or services.
Environmental quality standard specifies the maximum permissible value for a potentially hazardous substance/chemical in the environment/sample
Provides threshold/limits for parameters to protect the environment and public health
Serve as a basis for comparison; a reference point against which other measurements can be evaluated
Legal instrument that is imposed to remedy the environmental impact of emissions/discharges

## Slide 4: WHY THE STANDARD FOR AIR QUALITY
Air pollution affect the environment and human health
Increasing population and consumption and production patterns is adversely impacting on air quality
Air pollution is a national and a transboundary problem and diseases and disorders associated with exposure to air pollution tend to have wider scope of distribution
Other nations have taken steps to reduce air pollution and hence the need for all to make effort

## Slide 5: AIR QUALITY STANDARD
Two Standards:
Ghana Standard for Environment and Health Protection – Requirements for Ambient Air Quality and Point Source/Stack Emissions (GS 1236: 2019)
Ghana Standard For Environment and Health Protection – Requirements For Motor Vehicle Emissions (GS 1219:2018)

## Slide 6: Ghana Standard for Environment and Health Protection – Requirements for Ambient Air Quality and Point Source/Stack Emissions (GS 1236: 2019)

## Slide 7: AIR QUALITY STANDARD- GS 1236:2019
Recognizes the need to reduce air pollution from stationary, aerial, mobile and non-point sources to levels which minimize harmful effects on the environment and public health, paying particular attention to sensitive populations such as the elderly, children and pregnant women.
Provides for:
  Point source/stack emissions (Particulates, gases, metals): by facilities
  Fenceline (particulates, gases, metals etc depending on the type of undertaking): by facilities
  Ambient air quality (particulates, gases, aromatics, metals): by the Authority

## Slide 8: AIR QUALITY STANDARD- GS 1236:2019
  Specifies the requirements for ambient air quality and point source (stack) emissions
  Provides the various parameters that are required to be monitored and the permissible limits for releases into the environment
  Provides the standard test methods for measurement of each required parameter. However, other equivalent International Standard test methods or standard measuring instruments may be used but should be approved by the regulator
Equipment used for measurement shall be approved by the regulator

## Slide 9: AIR QUALITY STANDARD- GS 1236:2019
Point Source |  |  |  |  | 
Parameters | Maximum Limit |  |  |  | 
 | Solid fuels (Biomass, coal…) | Liquid fuels (Diesel, RFO…) | Gaseous fuels (CNG, LPG..) | Electrical | Incinerators
SO2(mg/m3) | 200 | 500 | 100 | 200 | 200
NOx(mg/m3) | 200 | 400 | 320 | 200 | 400
PM (mg/m3) | 50 | 50 | 50 | 50 | 70
Other Parameters | CO, HF, HCl, Hg & its compounds, Pb |  |  |  | 

## Slide 10: AIR QUALITY STANDARD- GS 1236:2019
 | Ambient Air Quality |  | 
 | Parameter | Maximum Limits | Averaging Time
1 | Sulphur Dioxide (SO2), μg/m3 | 150 | 24 hours
2 | Nitrogen Oxides (measured as NO2), μg/m3 | 150 | 24 hours
3 | PM10 , μg/m3 | 70 | 24 hours
4 | PM2.5, μg/m3 | 35 | 24 hours
5 | Lead, μg/m3 | 1 | 24 hours
6 | Other parameters: TSP, Black Carbon, Benzene |  | 

## Slide 11: AIR QUALITY STANDARD- GS 1236:2019
Fenceline |  |  | 
 | Parameter | Maximum Limit | Averaging Time
1 | Sulphur Dioxide (SO2), μg/m3 | 150 | 24 hours
2 | Nitrogen Oxides (measured as NO2), μg/m3 | 150 | 24 hours
4 | PM10, μg/m3 | 70 | 24 hours
5 | PM2.5, μg/m3 | 35 | 24 hours
Others | CO, H2S, TSP, HCl, Cd, Benzene, Hg, Mn, As, PAH, Xylene etc |  | 

## Slide 12: Ghana Standard for Environment and Health Protection – Requirements for Motor Vehicle Emissions (GS 1219:2018)

## Slide 13: VEHICULAR EMISSION STANDARD (GS 1219:2018)
Specifies the requirements for exhaust emissions of motor vehicles, tractors, farm equipment (such as combine harvester, etc.), mobile industrial/construction machines (such as excavators)
Do not apply to engines used on water bodies such as boats, jet skis and canoes using an outboard motor; aviation including helicopters and airplanes or stationary motors such as generators and corn mills
The Ghana Standard for Motor Vehicle Emissions was derived from the EURO II vehicle exhaust emission standard with some modifications to reflect local data collected by the Agency & Research institutions
Designed not to put too many vehicles off the road, to be revised over time to make more stringent

## Slide 14: VEHICULAR EMISSION STANDARD (GS 1219:2018)
Vehicles emissions are affected by:
  driving patterns,
  the vehicle type and age,
  fuel type and quality,
  road conditions,
  axel load,
  traffic speed and congestion
  altitude and other ambient conditions etc
All these areas need to be tackled to reduce vehicular emissions

## Slide 15: VEHICULAR EMISSION STANDARD (GS 1219:2018)
Classification
Standard classified according fuel type and the year of manufacture of vehicle
  Category A: vehicles that were manufactured before and during 1995
  Category B: vehicles that were manufactured after 1995.

## Slide 16: VEHICULAR EMISSION STANDARD (GS 1219, 2018)
Fuel Type | Category | Parameter | Requirements
Petrol/CNG/LPG | A | CO (%), max. | 3.5
 | B |  | 2.5
 | A | HC (ppm), max. | 800
 | B |  | 300
Diesel | A | Opacity (%), max. | 55
 | B |  | 40
Also for motor cycles |  |  | 

## Slide 17: VEHICULAR EMISSION STANDARD (GS 1219:2018)
Other Requirements
Equipment used for testing shall be approved by the Authority
Reports of motor emission levels of vehicles shall be presented to the appropriate authority as part of the requirements for issuance of road worthy certificate
A vehicle shall be deemed to have complied with the requirements of this Standard if after testing, the results show that emissions for all parameters as prescribed for the vehicle engine type and year of manufacture fall below the limits

## Slide 18: STANDARD DEVELOPMENT PROCESS
Formed Internal Committee from relevant departments in the Authority
Gathered data (in-house and external sources): EPA monitoring data, self-monitored data from industry, Research/studies, International standards especially from developing countries with similar geographical conditions
Checked for data integrity through verifications and validation
Selected relevant parameters based on their significant risk posed through indirect/direct risk to human health and the environment
Set the limits based on data gathered and adopted international standard where there were no data for Ghana
Compared parameters and permissible limits with international standards (WHO, IFC etc)

## Slide 19: STANDARD DEVELOPMENT PROCESS
Compiled the zero-draft standard
Organised National stakeholder workshop to review the zero-draft standard
National Technical Committee (NTC) formed by GSA with membership from academia, MDAs, MMDAs, private sector etc to review the zero draft
Revised draft standards from (NTC) reviewed by selected independent experts
Comments from selected reviewers reviewed by NTC and incorporated into the draft standards
Standard finalized, published and gazetted

## Slide 20: POLICIES FOR AIR QUALITY
Policy | 
The 1992 Constitution of the Republic of Ghana | The Constitution places responsibility on: the state, to take appropriate measures needed to protect and safeguard the national environment for posterity and seek co-operation with other states and bodies for the purposes of protecting the wider international environment for mankind (article 36(9)). every citizen to protect and safeguard the environment (article 41(k))
The National Environmental Policy (2012) | Gives directions on the constitutional mandate of Ghana to protect and safeguard the environment by detailing, among others, various strategic goals and objectives on sustainable resource use, impact management and holistic integrated planning It addresses air pollution as part of its broader environmental management goals - Pollution Prevention & Control: incorporates measures to control, reduce and prevent pollution in general and application of the polluter pays principle; Waste Management: using waste as resource; Energy Resources: promotes renewable energy; create public awareness on dangers of pollution

## Slide 21: POLICIES FOR AIR QUALITY
Policy | 
Environmental Sanitation Policy (2010) | Aims to improve public health and living standards through better waste management, sanitation infrastructure, and hygiene practices Outlines the framework for managing waste and maintaining a clean, safe environment to improve public health and well-being.
Industrial Policy | The policy emphasizes the need for cleaner production and environmentally sustainable industrial practices. ​ Key dimensions related to air pollution include: promotes the adoption of environmentally friendly technologies and improved manufacturing processes to reduce pollution. encourages the efficient use of raw materials, energy, and water in industry, which can help minimize emissions. ​ encourages industries to develop and implement self-regulatory measures on environmental management, which include strategies to reduce air pollution. ​

## Slide 22: POLICIES FOR AIR QUALITY
Policy | 
Transport Policy (2008) | The National Transport Policy of Ghana addresses air pollution primarily through strategies aimed at reducing greenhouse gas emissions and promoting sustainable transport practices. Areas include: Promotion of Sustainable Transport:Mainstreaming green infrastructure, climate change, and sustainability issues into transport sector activities. ​ Improved Vehicle Technologies:Undertaking research into vehicle and fuel technologies to identify those most appropriate for the region, with a focus on reducing emissions. ​ Traffic Management: Better traffic management and increased use of mass transit systems to reduce congestion and subsequent air pollution. ​ Integrated Land Use and Transport Planning: Encouraging mixed and integrated development of the built environment to reduce the need for travel and mitigate congestion-related air pollution. ​ Non-Motorized Transport (NMT):Integration of NMT facilities in transport infrastructure developments to promote walking and cycling, which are non-polluting modes of transport.
National Electric Vehicle Policy (2023) | Fulfils commitment to address climate change and its effect on humanity Promote the widespread adoption of electric vehicles Provide the framework for addressing key global and local issues associated with vehicles fitted with internal combustion engines (ICEs)

## Slide 23: POLICIES FOR AIR QUALITY
Policy | 
Energy Policy (2010) | The policy deals with various sub-sectors including: ensuring sustainable exploration, development and production of petroleum; increasing the proportion of renewable energy in the total energy mix; promoting waste-to-energy-by converting wastes generated from municipal activities, industrial operations and agriculture into energy; promoting energy efficiency and conservation
Climate Change Policy | The policy seeks to ensure a climate-resilient and climate-compatible economy while achieving sustainable development through equitable low-carbon economic growth for Ghana The three Focal areas: (1) effective adaptation, (2) social development and (3) mitigation Programme Areas identified to address the fundamental critical issues in climate change include: Increase carbon sinks & Minimize greenhouse gas emissions

## Slide 24: OTHER LEGAL & REGULATORY FRAMEWORK
Legislation | 
Environmental Protection Act, 2025, (Act 1124) | The Act established the EPA to regulate, protect, coordinate and exercise general oversight over matters relating to climate change and the environment. The functions include: Issue environmental permits for undertakings to control the volume, types, constituent, and effects of waste discharges, emissions, deposits, noise or any other source of pollution and of substances which are hazardous or potentially dangerous on the quality of the environment and human health Carry out environmental quality monitoring to develop a database for policy formulation and implementation Collaborate with relevant institutions to develop a comprehensive national database on the environment and environmental protection Prescribe of environmental quality standards and guidelines relating to the pollution of air, water, land, and any other form of environmental pollution in consultation with relevant stakeholders

## Slide 25: OTHER LEGAL & REGULATORY FRAMEWORK
Legislation | 
Environmental Protection Act, 2025, (Act 1124) | Promote of research and carrying out studies, surveys and analyses and disseminate information on the findings for the improvement and protection of the environment Create awareness on environmental issues
Environmental Protection (Environmental Assessment) Regulation, 2025 (LI 2504) | Regulates the conduct of environmental assessment and the issuance of environmental permits in Ghana. Makes it mandatory for all undertakings likely to have adverse effect on the environment to register with the Authority and obtain an Environmental Permit. Details the procedure, requirements and conditions for obtaining an Environmental Permit. Applicants are also to indicate a clear commitment to climate change mitigation & adaptation, biodiversity conservation, pollution control and prevention

## Slide 26: OTHER LEGAL & REGULATORY FRAMEWORK
Legislation | 
Hazardous, Electronic and Other Wastes (Classification), Control and Management Regulations, 2016 (LI 2250) | Regulates the classification, control and management of waste. Establishes a procedure for the listing of waste management activities that do not require a Waste Management Permit. the requirements for the establishment of take-back systems; the general duties of waste generators, transporters and managers; and the requirements for the disposal of wastes
Environmental Protection (Air Quality management) Regulations, 2025 (LI2507) | Improve air quality in the country by controlling emissions from various sources including industry & motor vehicle, ensuring compliance with the GS1236 & GS 1219, etc. It requires: Development of an Air Quality Management Framework which would provide for the development of an air quality policy, AQMP by District Assemblies Establishment of a National Air Quality Information Management System with dashboard to facilitate routine reporting Harmonisation of sampling protocols and test methods to align with the GS 1236 Vehicles to be tested and issued with Emission Compliance Certificates to be used as requirement for road worthy certificate Provides sanctions for non-compliance

## Slide 27: OTHER LEGAL & REGULATORY FRAMEWORK
Legislation | 
Local Governance Act 2016, Act 936 | Provides for local governance in accordance with the Constitution and the National Development Planning System. Defines and regulates the planning procedures of District Assemblies and other related matters Mandates the Assemblies to enact bye-laws to abate nuisances eg. open burning of wastes
GRA Customs Division Law (Act 634) of 2012 | Age-based tax system; penalty on cost, insurance & freight of over-aged vehicles, 10-12 years pays 5% (2.5%)penalty on the CIF 12-15 years: 20% (10%) Over 25 years: 50% (15%)

## Slide 28: OTHER LEGAL & REGULATORY FRAMEWORK
Legislation | 
Ghana Road Transport Regulations, 2012, LI 2180 | Regulates the registration of vehicles and the provides other conditions required for vehicles to ply on the roads Vehicles to be fitted with pneumatic tyres labelled temperature class ‘A’ or ‘B ‘for hot or normal weather areas and not Type ‘C’ tyres meant for cold areas The tyres should be of specified size to withstand the maximum permissible load Tyres more than 4 years from the date of manufacture shall not be used Tyres should not be over/under inflated Vehicles must not exceed the permissible axle load and gross vehicle weight

## Slide 29: OTHER LEGAL & REGULATORY FRAMEWORK
Standards | 
Ghana Standard for Environment and Health Protection – Requirements for Ambient Air Quality and Point Source/Stack Emissions (GS 1236, 2019) | Specifies the requirements for ambient air quality and point source (stack) emissions and gives guidelines for discharge into the ambient environment. It provides the various parameters that are required to be monitored by undertakings and the standard test methods for measurement of each required parameter.
Ghana Standard for Environment and Health Protection – Requirements for Motor Vehicle Emissions (GS 1219, 2018) – | Specifies the requirements for exhaust emissions of motor vehicles, tractors, farm equipment (such as combine harvesters, etc) and mobile industrial/construction machines (such as excavators). It requires monitoring of emission levels to be carried out every year for private motor vehicles and every six months for commercial vehicles.

## Slide 30: OTHER LEGAL & REGULATORY FRAMEWORK
International Obligations | 
Commitments to the Sustainable Development Goals | Goal 3 (Target 3.9) seeks to substantially reduce the number of deaths and illnesses from hazardous chemicals and air, water and soil pollution and contamination Goal 11 (Target 11.6) aims to reduce the adverse per capita environmental impact of cities, by paying special attention to air quality and municipal and other waste management, and Goal 13: seeks to combat climate change and its impacts.

## Slide 31: SOME AIR QUALITY MANAGEMENT EFFORTS BY EPA
Established monitoring locations to monitor and gather data on ambient air quality
Created air quality database
As part of the EA process to permit undertakings, entities are required to monitor air emissions (from point sources) and air quality at the fence line at defined frequencies and report in their quarterly environmental monitoring reports and other environmental reports to the Authority.
Point source air emissions from industry are regulated through the installation of appropriate pollution control systems
The Authority in collaboration with GSA and other stakeholders developed the Ghana Standard for point source emissions and ambient air quality (GS 1236:2019 ) and motor vehicles emissions (GS 1219:2018) using, baseline air quality data collected from the monitoring activities.
Air Quality Regulations have been developed to facilitate effectitive air quality management

## Slide 32: SOME AIR QULAITY MANAGEMENT EFFORTS BY EPA
Organise capacity building programmes for staff and other stakeholders:
Low Emission Analysis Platform (LEAP-IBC) tool to estimate the level of emissions from different sources such as the energy, industrial, agricultural, and waste sectors, and their contribution to urban air quality.
Air quality modelling and forecasting to build capacity on predicting air quality trends and outcomes
Household Air Pollution and monitoring (beneficiaries included NGOs public institutions, academia etc.).
Proper management and recycling practices for Actors in the electronic waste management value chain in order to prevent burning.
Resources Use Effciency and Cleaner Production (RECP), Environmental monitoring and reporting, EIA procedure for Industries

## Slide 33: SOME AIR QULAITY MANAGEMENT EFFORTS BY EPA
Capacity Building Programmes (Contd)
  Consultants on the EIA procedure to improve quality of the reports
  District Assemblies on waste management, the Ghana Standards, etc
  Artisans on biogas construction
Donor funded projects to promote efficiency:
  SAG project on greeen economy: institutional stoves for gari, fish & pito processors
  UNEP project on boiler efficiency for industry and small scale palm oil producers
  Technical guidelines to guide operations of ULAB industries
  Promotion of industrial symbiosis to reduce waste to landfill

## Slide 34: SOME AIR QUALITY MANAGEMENT EFFORTS BY EPA
Support to Industry
  Developemnt of formats and guidelines for reporting
  Implementation of Akoben programme to drive self compliance
The EPA has collaborated with other stakeholders to develop policy interventions including:
  Fuel economy, soot free buses (use CNG) and electric mobility
  National Fuel Quality Standards led by National Petroleum Authority
  National Vehicle Specification led by Ministry of Trade and Industry
  National standards for biomass cookstoves.
  Phase out of Lead in fuel

## Slide 35: AIR QUALITY MANAGEMENT EFFORTS BY EPA
Developed an Air Quality Management Plan (AQMP) as part of the efforts to reduce pollution.
Support to research on source contributions

## Slide 36: CHALLENGES
Inadequate implementation of the available policies & legal/regulatory frameworks
Inadequate coordination among stakeholders thus working in silos & leading to duplication of efforts
Continuous use of Age-based taxation system; penalty on cost, insurance & freight on overaged vehicles which is not deterent
Delay in enforcing vehicular emissions standard
High cost of monitoring equipment to extend monitoring

## Slide 37: WAY FORWARD
Stakeholders need to improve implementation of the available policies & legal/regulatory frameworks
Enforcement of air quality regulations to facilitate the enforcement of the standard and effective air quality management
Effective collaboration/partnership with stakeholders across all sectors
Enforcement of the EA Regulations to ensure permitted underatkings comply with requirements
Collaboare with stakeholders to implement the AQMP developed to manage air pollution in Greater Accra Region
Finalise revision and enforce standards

## Slide 38: One Planet ! One Humanity! One love!
THANKS FOR YOUR ATTENTION